Difference between Von Neumann and Harvard Architecture
        BY:J PHANI KUMAR

---
Harvard Architecture
In Harvard architecture, the CPU is connected with both the data memory (RAM) and program memory (ROM), separately.
Harvard Architecture

---
Von Neumann Architecture
In Von-Neumann architecture, there is no separate data and program memory. Instead, a single memory connection is given to the CPU.

---
HARDWARE COMPONENTS
- HARVARD :It requires more hardware since it will be requiring separate data and address bus for each memory.
- VON-NEUMANN:In contrast to the Harvard architecture, this requires less hardware since only a common memory needs to be reached.

---
Space requirements
- HARVARD:This requires more space.
- Von-Neumann Architecture requires less space.

---
Speed of execution
- HARVARD:Speed of execution is faster because the processor fetches data and instructions simultaneously .
- VON-NEUMANN:Speed of execution is slower since it cannot fetch the data and instructions at the same time.

---
Space usage
- HARVARD:It results in wastage of space since if the space is left in the data memory then the instructions memory cannot use the space of the data memory and vice-versa.
- VON-NEUMANN:Space is not wasted because the space of the data memory can be utilized by the instructions memory and vice-versa.

---
Controlling
- HARVARD:Controlling becomes complex since data and instructions are to be fetched simultaneously.
- VON-NEUMANN:Controlling becomes simpler since either data or instructions are to be fetched at a time.

---
THANKYOU